## Slide 1: Introducing SiGNUM™ incremental encoders
20 µm pitch scale system
Functional safety certified (PLd)
Robust readhead sealed to IP64
High max. operating temperature
Linear speeds up to 12.5 m/s
Notes: Please read the notes below:
SiGNUM is Renishaw's high accuracy, non-contact 20 µm incremental encoder system comprising an Sr readhead and Si interface. It is sealed to IP64 and offers speeds up to 12.5 m/s and resolutions down to 5 nm, and reads a variety of linear and rotary scales with IN-TRAC auto-phase optical reference marks. SiGNUM is extremely easy to use with calibration at the push of a button and free diagnostic software, yet it offers a level of performance previously available only from more delicate fine pitch encoders with an SDE of typically <±30 nm at temperatures up to +85 °C.

## Slide 2: Value to you
Functionally safe
Robust
High speed
Increased performance
Easy set-up
Value
Notes: Please read the notes below:
Functionally safe: Ensures maximum safety and piece of mind by minimising inherent risk of failure.
Robust: SiGNUM readheads are sealed to IP64 for harsh machine tool environments.
High Speed: Allows faster processes and higher throughput.
Increased performance: High functionality, accuracy and precision allows designers greater flexibility.
Easy set-up: Set-up and calibration, with support from optional SIGNUM diagnostic software, streamlines production-line installation and subsequent servicing.

## Slide 3: Specifications
Functional safety certified* (compliant with ISO 13849-1)
Both 20 µm pitch linear and rotary scales available
Compact readhead size: 36 mm x 16.5 mm x 14.8 mm
Linear resolutions to 5 nm and linear speeds to 12.5 m/s
Rotary angular speeds to 4600 RPM
Choose FANUC serial comms or dual analogue / digital outputs
Linear system accuracy to ± 1 µm/m
Rotary system accuracy to ±1 arc second
Set-up LEDs and SiGNUM diagnostic software
* See functional safety supplement for instructions on installation, available for download on the Renishaw.com website
Notes: Please read the notes below:
The functional safety supplement can be found at the following address:
http://resources.renishaw.com/en/details/data-sheet-signum-functional-safety-supplement--66509

## Slide 4: Real-life applications
ABTech Manufacturing creates five-axis platforms for nanometre/sub-arc second processing around its ultra-precision air bearings
ABTech selected SiGNUM for an air-bearing optical metrology station requiring high resolution optical encoder feedback for multiple linear and rotary axes
“
“
This being a metrology system, we were most concerned about thermal stability. The Invar® scales were a perfect fit for this application. Accuracy, price, ease of use and physical size were key factors for ABTech in selecting a position encoder. The advanced SiGNUM system meets all of these criteria
Notes: Please read the notes below:
Please use link below for further details (paste following into browser):
http://www.renishaw.com/encodercasestudies

## Slide 5: SiGNUM basic principles
AND
Readhead sensor uses patented filtering optics
All digital SiGNUM interfaces offer analogue output as standard
Optical filtering, digital signal processing and the readhead’s IP64 rating provide exceptional dirt immunity – ideal for machine tool
Ease of set-up courtesy of LED indicators and built-in CAL routine with optional diagnostic software available
Notes: Please read the notes below:
SiGNUM open-optical encoder systems combine IP64 sealing, patented filtering optics and the latest analogue and digital signal processing to provide exceptional dirt immunity. SiGNUM encoders are ideal for machine tool applications requiring resistance to coolant splashes, metal swarf and other contaminants.
** Slide animates the scale and output waveform together – the presenter should allow several seconds for this to run**

## Slide 6: SiGNUM readhead options
Functionally safe
IP64 rating offering excellent dirt immunity
Resolutions from 5 µm to 5 nm
FANUC serial comms
0 °C – 85 °C
SiGNUM
Notes: Please read the notes below:
SiGNUM is a 'recoverable readhead' that offers 'wipe clean' recovery from coolant splashes or floods. An IP rating of IP64, high immunity to water, oil and dust and operating temperatures of up to +85 °C and speeds of 12.5 m/s mean that SiGNUM is ideal for more challenging applications whilst offering performance comparable with fine pitch glass scales.

## Slide 7: SiGNUM linear scales
Lengths to 1.5 m
±1 µm/m accuracy at 20 °C and near-zero CTE (Invar)
Mounting by adhesive or clips
RELM spar
RSLM spar
Lengths to 5 m
±4 µm accuracy over 5 m at 20 °C
Mounting by adhesive or clips mounting
Notes: Please read the notes below:
RSLM is a stainless steel spar scale featuring 20 µm pitch and a variety of IN-TRAC optical reference mark options, including regularly spaced for customer selection or single reference at the centre or close to the end. It is comparable to fine pitch glass scales and offers a total accuracy (including slope and linearity) better than ±4 µm over a 5 m length. It can also be coiled for simple storage and handling yet once uncoiled behaves as a spar scale. System designers can choose between specially formulated adhesive tape or mechanical clips to suit mounting requirements. Both mounting methods allow for independent thermal expansion to that of the substrate.
RELM is a spar scale manufactured from ZeroMet™, a low expansion nickel/iron alloy, featuring a 20 µm pitch. It is comparable to fine pitch glass scales and offers a total accuracy (including slope and linearity) better than ±1 µm over a 1.13 m length. ZeroMet has a thermal expansion coefficient of approximately 0.6 µm/m/°C over the temperature range of 0 °C to 30 °C. System designers can choose between specially formulated adhesive tape or mechanical clips to suit mounting requirements. Both mounting methods allow for independent thermal expansion to that of the substrate.

## Slide 8: SiGNUM rotary scales
RESM ring
Low profile scales with standard sizes up to Ø550 mm
Graduation accuracy to ± 0.5 arc second (Ø550 ring)
Patented taper mount simplifies integration and eliminates installation errors
Ultra-high installed accuracy to ±1 arc second
Low-distortion profile with standard sizes to Ø417mm
Flange mounted with easy 4-point adjustment method
REXM ring
Notes: Please read the notes below:
RESM is a one-piece stainless steel ring with 20 µm pitch graduations marked directly on the periphery, featuring the IN-TRAC™ optical reference mark. Two versions are available in a wide range of sizes (Ø52 mm to Ø550 mm). ‘A' section rings, which offer an impressive installed accuracy, feature a taper mount system which reduce the need for highly toleranced machined parts and eliminate eccentricity. ‘B' section thin rings, which are low inertia and mass, are also available. Both 'A' and 'B' section rings have a large internal diameter for flexible integration. The non-contact format eliminates backlash, shaft wind-up (torsion) and other mechanical hysteresis errors that are inherent in traditional enclosed encoders.
REXM is a one-piece stainless steel ring with 20 µm pitch incremental graduations marked directly on the periphery, featuring the IN-TRAC optical reference mark. Its larger cross-section allows for the reduction in all installation errors apart from eccentricity, which is easily corrected using a DSi (Dual Signal Interface) and two readheads. Featuring total installed accuracy up to ±1 arc second, zero coupling losses, and exceptional repeatability. REXM is available in a range of sizes (Ø52 mm to Ø417 mm) and line counts, all of which have a large internal diameter for flexible integration. The non-contact format eliminates backlash, shaft wind-up (torsion) and other mechanical hysteresis errors that are inherent in traditional enclosed encoders.

## Slide 9: The SiGNUM Solution
Functional safety certified
IP64 rating for exceptional dirt immunity and resistance to coolant splashes
High performance system for linear speeds to 12.5 m/s
Higher operating temperatures
Choose from range of highest-accuracy linear and rotary scales
Any questions?
Notes: Please read the notes below:
Any questions? slide
Feel free to amend for your individual presentation; this should summarise your main points (no more than 5-6 total)